## Slide 1: Case Study:
Liam Davis
Mapping a Path to Net Zero for a Retail Business

## Slide 2: Solar Feasibility
Are Photovoltaic Solar Systems Viable at the Retail Locations?

## Slide 3: Factors to Consider for On-Site Solar
Cost
Does PV Solar make financial sense for every site?
How much Solar is most economical?
Location
How strong is solar radiation in each location?
Are there any obstructions, such as tall buildings or trees which may block sunlight?
Energy Usage Profile
When is most Energy needed?
Does this correlate with when the sun is shining?
Regulations
Is a permit or planning approval needed?
Does grid connection need to be approved?
Building Considerations
Is there enough roof space?
Is the roof strong enough to hold the solar system desired?

## Slide 4: Solar Feasibility: NSW
The graphs below show the amount of money saved over the life of the PPA by adding each additional kW of Solar, to each site in New South Wales. Data for both a 100% Renewable approach and a 50% Renewable approach are included.
Chart: Money Saved for each additional kW of Solar (100% Renewable Approach)
Chart: Money Saved for each additional kW of Solar (50% Renewable Approach)
As is clear from the graphs, even based on a conservative price estimate of $1000/kW, the first 111 kW of solar pay for themselves within the 5-year life of the PPA. Based on the same conservative price estimate, and an estimated system lifespan of 30 years, it was determined that a system of up to 185kW of Solar at each NSW site would save more money than its amortized cost. Hence a 185kW Solar system at each NSW site is economically optimal.

## Slide 5: Solar Feasibility: QLD
Below are those same graphs of Dollars saved per additional kW of solar for Queensland.
Chart: Money Saved for each additional kW of Solar (100% Renewable Approach)
Chart: Money Saved for each additional kW of Solar (50% Renewable Approach)
Again, it is clear from the graphs that even based on a conservative price estimate of $1000/kW, the first 97kW of solar save more money than they cost, even within the short 5-year life of the PPA. Using this price estimate and a 30 year estimated lifespan, it was determined that for a 100% Renewable approach, a system of up to 215kW of Solar at each QLD site would save more money than its amortized cost, and for a 50% Renewable approach this number is 162kW. Hence in the context of a 100% Renewable approach a 215kW system at each QLD site would be economically optimal, and for a 50% Renewable approach the economically optimal Solar system size is 162kW.

## Slide 6: Solar Feasibility: VIC
Victoria, with its peak loads similar to Queensland, but much higher overnight loads is a different picture to the other two states.
Chart: Money Saved for each additional kW of Solar (50% Renewable Approach)
Chart: Money Saved for each additional kW of Solar (100% Renewable Approach)
As shown above, any solar system installed in Victoria would likely take longer than the period of the PPA to recoup its cost. However, amortizing the estimated $1000/kW cost over an estimated 30-year lifetime, any solar system up to 256kW at each site in VIC would save more money than it cost. Therefore, a 185kW Solar system at each NSW site is economically optimal in Victoria.

## Slide 7: On-Site Solar Recommendations: Summary
100% Renewable
NSW
185kW PV Solar System at each site
QLD
215kW PV Solar System at each site
VIC
256kW PV Solar System at each site
50% Renewable
NSW
185kW PV Solar System at each site
QLD
162kW PV Solar System at each site
VIC
256kW PV Solar System at each site

## Slide 8: How Much Carbon Would This Save?
Based on the solar systems recommended, the 100% renewable approach would save 611,149.14 Tonnes of Carbon from entering the atmosphere each day, while the 50% Renewable approach would save 571,757.75 Tonnes of Carbon per day. The monetary value of this saving as Australian Carbon Credit Units, based on the price on the 16/06/2025 of $35.75, is $21,848,581.6 per day for the 100% Renewable approach, and $20,440,339.6 for the 50% Renewable approach. This is broken down by state in the graphs below.
Chart: CO2 Emissions Savings (Tonnes)
| 100% Renewable Strategy | 50% Renewable Strategy
NSW | 247384.368 | 247384.368
QLD | 159795.2412 | 120403.8562
VIC | 203969.5258 | 203969.5258
Chart: CO2 Emissions Savings ($ of ACCU value)
| 100% Renewable Strategy | 50% Renewable Strategy
NSW | 8843991.156 | 8843991.156
QLD | 5712679.8729 | 4304437.8577
VIC | 7291910.5459 | 7291910.5459

## Slide 9: Power Purchase Agreement
Pairing on-site solar with purchased renewable energy

## Slide 10: Renewable Percentage in the PPA
The recommended renewable percentage nominated in the Power Purchase Agreement is based on the economically optimal mix of on-site solar and energy purchased from a retailer. They are as below.
100% Renewable:
100% nominated renewable percentage
A nominal amount of 6,366.75MWh over the life of the contract
50% Renewable:
11.52% nominated renewable percentage
A nominal amount of 747.09MWh over the life of the contract

## Slide 11: Energy Retailer Comparison
For the recommended amounts of PV Solar, the cost of the remaining electricity, when purchased from each of the energy retailers, over the life of the PPA is laid out below.
Chart: Energy Retailer Price Comparison (100% Renewable Strategy)
| A | B | C | D | E | F
NSW | 23040390.656 | 21703237.184 | 24302881.424 | 23510860.544 | 22446070.112 | 23312618.192
QLD | 8227034.9152 | 8184896.8448 | 8740344.9296 | 8425783.0272 | 8247359.8336 | 8170719.2
VIC | 29122157.0534 | 29825222.8666 | 31216589.9918 | 29946117.696 | 29662132.2096 | 28601016.8558
Chart: Energy Retailer Price Comparison (50% Renewable Strategy)
| A | B | C | D | E | F
NSW | 19424059.904 | 18062244.704 | 20785875.104 | 19968785.984 | 18879333.824 | 19696422.944
QLD | 7570835.511 | 7523221.8918 | 8174269.3581 | 7818748.1114 | 7617180.6784 | 7506179.0483
VIC | 25408521.8534 | 26086262.3666 | 27604951.7418 | 26308736.696 | 25999425.9096 | 24887520.8058
For both the 100% Renewable, and 50% Renewable approaches, Retailer B is the cheapest option if energy demand remains consistent, at $59,813,356.90 and $51,671,729 respectively.

## Slide 12: Summary

## Slide 13: Renewable Strategy Summary: 100% Renewable
Solar
185kW per Site in NSW
215kW per Site in QLD
256kW per Site in VIC
Chart: 
| On Site Solar | Purchased Renewable Energy
 | 5110352.64 | 6366747.36
Energy Make Up
44.53% Solar
55.47% Purchased Renewable from Retailer B
Carbon Savings
174,819 Tonnes/Year Overall
111,118 Tonnes/Year From On-Site Solar
$3,972,469/Year of ACCUs Saved by On-Site Solar

## Slide 14: Renewable Strategy Summary: 50% Renewable
Solar
185kW per Site in NSW
162kW per Site in QLD
256kW per Site in VIC
Chart: 
 | 4991465.16 | 747084.84 | 5738550
Energy Make Up
43.49% Solar
6.51% Purchased Renewable from Retailer B
50% Purchased Non-Renewable from Retailer B
Carbon Savings
87,409 Tonnes/Year Overall
103,955 Tonnes/Year From On-Site Solar
$3,716,425/Year of ACCUs Saved by On-Site Solar

## Slide 15: Estimated Costings
100% Renewable
$24,486,065/Year
50% Renewable
$22,253,042/Year
*Annual nationwide cost including amortized cost of PV Solar System (Estimated at $1000/kW, with lifespan of 30 years). Demand is assumed to be consistent over the next 5 years. Not including potential for storage (Estimated at 445,579kWh/Year and 341,232kWh/Year for 100% Renewable and 50% Renewable respectively) or monetary value of equivalent ACCUs.